## Slide 1: FPGA Development in VHDL
Practicals

## Slide 2: Practical 1: hello world
Wire LED 0 to switch 0.
Wire LED 0 to switch 0 and LED 1 to switch 1.
Wire LED 0 to switch 0 and LED 1 to switch 1 using a std_logic_vector.
Wire LED 0 to switch 1 and LED 1 to switch 0 using a std_logic_vector.

## Slide 3: Practical 2: Asynchronous logic
Implement the following logic functions using switches as the input and an LED as the output:
  a XOR b
  The following Karnaugh maps:
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 0
01 | 1 | 1 | 1 | 1
11 | 0 | 1 | 0 | 0
10 | 0 | 1 | 0 | 0
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 0
01 | 1 | 1 | 1 | 0
11 | 0 | 1 | 0 | 0
10 | 0 | 0 | 0 | 0

## Slide 4: Practical 3: Muxes
Write a mux to select between switch 1 and switch 2 using switch 0 with LED 0 as the output using:
  A) a when-else statement
  B) a with-select statement
Implement the last logic function in Practical 2 using a with-select statement.

## Slide 5: Practical 4: Processes
Wire the LEDs to the switches using a process.
Experiment with assignment order.
Adapt the example so the LEDs are all off unless a button is pressed.
Implement a rising edge triggered flip flop using a button as the clock.
Implement the last logic function from Practical 2 with a flip flop.
Implement the same logic function using a case statement.

## Slide 6: Practical 5: Flip Flops
Implement a flip flop with a synchronous set and reset. Use buttons for the clock, set and reset. Use a switch for the input and an LED for the output.
Implement the same without using ‘elsif’ or ‘else’.
Implement an asynchronous reset

## Slide 7: Practical 6: schematics and timing report
Implement two flip flops chained together.
In Vivado, view the synthesised schematic and timing report.

## Slide 8: Practical 7: half/full adder
Implement a half adder component and instantiate it in a top level VHDL file.
Implement a self-checking test bench for the half adder.
Repeat with a full adder.

## Slide 9: Practical 8: multi-bit adder
Implement a generic-width adder using the full adder component from Practical 7 and a generate statement.
Verify with a self-checking test bench.
Implement the same functionality using the ‘+’ operator.
Investigate bit-growth and build an adder using ‘+’ that doesn’t overflow.

## Slide 10: Practical 9: Counter
Using a counter, generate a 1 cycle pulse that occurs every N (power of 2) clock cycles. Make N generic.
Use the pulse to toggle an LED.

## Slide 11: Practical 9: Counter
Using a counter, generate a 1 cycle pulse that occurs every N (power of 2) clock cycles. Make N generic.
Use the pulse to toggle an LED.
Now implement without comparing all the bits of the counter.

## Slide 12: Practical 10: DSP Multipliers
Write VHDL to infer a DSP slice to perform a multiply. Use switches as input and LEDs as output. Use the DSP48E1 user manual for reference.
Produce the same implementation by instantiating a DSP48E1 primitive directly.

## Slide 13: Practical 11: ROM
Write VHDL to infer a ROM.
Use the ROM to generate a pattern on the LEDs.
Change the ram_style attribute to try distributed and block RAMs.

## Slide 14: Practical 12: RAM
Write VHDL to infer a RAM.
Use switches for the address and data input. Use buttons for write enable. Use LEDs for data output.
Change the ram_style attribute to try distributed and block RAMs.

## Slide 15: Practical 13: FIFO
Use the Vivado IP generator to create a custom FIFO.
Use switches as the input, LEDs as the output and buttons for write, read and reset.
Does it work reliably as intended? If not, why not?

## Slide 16: practical 14: FSM
Using an FSM implement a combination lock.
Use the four direction buttons as code input and the middle button a ‘clear’.
Use an LED to indicate if the lock is open or closed.
Extensions:
  Set a new code. Timeout. Use LEDs to indicate time remaining.